## Slide 1: Water Quality and Environmental Systems Modeling
Todd Steissberg, PhD, PE
Research Environmental Engineer
Team Lead, Ecohydrology
Environmental Laboratory
Engineer Research and Development Center (ERDC)
U.S. Army Corps of Engineers
ASU Seminar
February 21, 2023
UNCLASSIFIED
UNCLASSIFIED
Hydrologic
Engineering
Center

## Slide 2: ASU-ERDC Engineering With Nature (EWN) Collaboration
Team members:
  Rebecca Muenich1
  Todd Steissberg2
  Ting Liu1
  Joanna Curran4
  Isaac Mudge5,2
  Lauren Melendez2
  Billy Johnson6,2
  Jodi Ryder2
  Rose Shillito3
  Selcuk Candan1
  Amber Wutich1
  Todd Swannack2
  1ASU
  2USACE-ERDC-EL
  3USACE-ERDC-CHL
  4USACE Seattle District
  5USACE New Orleans District
  6LimnoTech

## Slide 3: ASU-ERDC Engineering With Nature (EWN) Collaboration
Maintaining water quality while managing water resources is a difficult goal to achieve, due to:
  Extreme conditions: precipitation, flow, temperature, and runoff containing heavy loads of nutrients and other contaminants
  Multiple drivers and potential control points throughout the system
Water quantity and quality is influenced at many points as it flows through the watershed:
  Rain: Source areas in the uplands (precipitation, snow melt, agricultural sources, springs, etc.)
  Runoff: Transport across the landscape (runoff and sub-surface flow)
  Rivers: Flows into and through stream networks
  Reservoirs: Flows into reservoirs or other water infrastructure
Basins across the U.S. face extremes on both ends of the climate spectrum: flooding and drought
Management of upland landscapes (e.g., agricultural lands) or land adjacent to reservoirs, levees, and other water infrastructure systems is often not aligned with the infrastructure management itself, particularly neglecting to ensure water quality alongside water quantity.

## Slide 4: ASU-ERDC Engineering With Nature (EWN) Collaboration
There are many land-use types across the basins that USACE and other government agencies manage
Agricultural lands represent the majority of non-government owned land in the U.S.
  These lands are often co-located with water resources infrastructure and are actively managed, often with practices similar to NNBF.
  Coordination and eventual integration of USACE activities (particularly EWN) with upland agricultural management will help reduce system-wide inefficiencies and produce more synergistic outcomes for water quantity and quality.
Agricultural lands and water resources infrastructure in the Continental U.S.
(a) Agricultural lands from USDA (green = pasture/range, orange = cropland).
(b) Reservoir locations from USACE.
(c) Levee locations from USACE.

## Slide 5: ASU-ERDC Engineering With Nature (EWN) Collaboration
Solutions:
  Improved management of existing water resources infrastructure
  Natural and Nature-Based Features (NNBF) to improve the health and resiliency of ecosystems, communities, and infrastructure
How do we quantify and realize landscape-scale benefits to water quantity and quality in integrated and complex systems?
  We need a modeling framework that can take complex site-specific interactions and upscale these disparate interactions on a system-wide and aggregated scale.

## Slide 6: ASU-ERDC Engineering With Nature (EWN) Collaboration
Examples of these coordination activities include:
  Reservoir management with upland agricultural land management
  Coordinating NNBF solutions (e.g., levee plantings and setbacks) with existing agricultural land management and conservation practice implementation.
Our primary objectives in the first three years are to:
  Assess the feasibility of this approach through nationwide data scoping and stakeholder engagement
  Develop the modeling and data science tools and methods to inform best practices and enable USACE to locate and evaluate opportunities for NNBF across USACE-managed systems.
This project will:
  Address large knowledge gaps regarding how these systems work
  Identify new strategies to advance where, when, and how these integrated landscapes can be better managed to mimic larger-scale, natural processes for a system-wide EWN approach that utilizes new and state-of-the art modeling and data science techniques.

## Slide 7: ASU-ERDC Engineering With Nature (EWN) Collaboration
Objectives:
Identify the potential for integrated management of upland areas and traditional water resources infrastructure (e.g., reservoirs, levees) across the U.S.
Select and model at least one of these systems at the watershed-scale, based on data scoping and stakeholder preferences from objective 1.
Implement, test, and monitor the performance of at least one nature-based solution in the selected system.
Develop methods to transfer learning and emulation modeling techniques to simulate and understand processes driving and controlling water quantity and quality in these integrated systems.
Apply the models, methods, and data from objectives 1-4 to demonstrate the applicability of this integrated system management in basins across the U.S.

## Slide 8: Water Quality Modeling

## Slide 9: Modeling Definitions
Mathematical modeling is the process of developing a mathematical representation of a system using mathematical concepts and techniques to describe the processes, interactions, and parameters of that system.
Computer modeling is the process of developing mathematical algorithms that describe a system and then developing the computer code to simulate them.
Modeling vs. Simulation:
  Modeling is the process of building a model
  Simulation is the process of using a mathematical model to study the behavior of a system for a particular time period.
Source: https://en.wikipedia.org/wiki/Flowchart

## Slide 10: Computer Models & Programming
Early computer models were custom-developed applications programmed for a specific purpose, such as a water quality model of a particular lake or reservoir.
The first mathematical water quality model was developed by Streeter and Phelps in 1925. It predicted the dissolved oxygen “sag curve” in rivers.
In the 1960’s, computer models began to be developed. By the early 1970’s, general-purpose models began to emerge.
Today’s general-purpose water resources models, e.g., HEC-RAS, HEC-ResSim, and CE-QUAL-W2, typically do not require the modeler to do any programming.
  CE-QUAL-W2 is a general-purpose model, but it allows custom computations through modifying and enhancing the source code.
  HEC-ResSim allows custom computations through “scripting.” Modelers cannot alter the source code.
  Scripting (Python, R, MATLAB) is increasingly used for visualization and analysis of the results.
A 48-hour computer simulation of Typhoon Mawar using the Weather Research and Forecasting model.
Source:
https://en.wikipedia.org/wiki/Computer_simulation

## Slide 11: Water Quality Modeling
Water quality modeling combines mathematical descriptions of the physical and biogeochemical processes to characterize behavior of a waterbody or water resource.
Water resource and water quality models have been developed to understand and predict the processes in reservoirs, rivers, and watershed runoff.
The following fields comprise the body of knowledge required for accurate water quality modeling and analysis:
  Hydrodynamics (physical limnology)
  Meteorology
  Aquatic chemistry (chemical limnology)
  Aquatic biology (biological limnology)
  Geology (sedimentation, sediment settling, resuspension, and transport)
  Mathematics and numerical methods
  Statistics
Flows influence water quality
Water quality must influence flows

## Slide 12: Benefits of Water Quality Modeling
Interpolation
  Observed data is sparse in space and time.
  Interpolation addresses questions like:
    Where are the best locations for sampling?
    Where are the most severe water quality problems occurring?
Extrapolation
  Forecast water quality in the future.
  Predict water quality for different water management scenarios
  Extrapolation answers questions like:
    How will the watershed function under different climate forcing conditions?
    How will the ecosystem respond if flow allocations are changed, hydropower withdrawals increased, and releases altered to meet ecosystem restoration targets (e-flows)?
Improved understanding of the system.
Dworshak Dam, Idaho
Detroit Dam, Oregon

## Slide 13: Systems Modeling: Guiding Principles
George Box:
  ... all models are approximations. Essentially, all models are wrong, but some are useful. However, the approximate nature of the model must always be borne in mind....
  Paraphrased:
    “All models are wrong, but some are useful.”
Albert Einstein:
  It can scarcely be denied that the supreme goal of all theory is to make the irreducible basic elements as simple and as few as possible without having to surrender the adequate representation of a single datum of experience.
  Paraphrased:
    “Everything should be made as simple as possible, but no simpler.”
Hans Albert Einstein (Hydraulic Engineer):
  You can assume anything you want. The water won’t!
  Moral: Be careful with your assumptions.
Albert Einstein, said of his son’s career, “He is working on a more difficult problem.”

## Slide 14: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?

## Slide 15: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?
It seems simple: centrifugal force should cause the tea leaves to collect along the sides of the cup. But do they?

## Slide 16: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?
It seems simple: centrifugal force should cause the tea leaves to collect along the sides of the cup. But do they?
Albert Einstein solved this problem in 1926 in a paper he wrote on meandering rivers. Einstein was the first person to describe how helical flow helps to determine the length and migration of meander bends in rivers.

## Slide 17: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?
It seems simple: centrifugal force should cause the tea leaves to collect along the sides of the cup. But do they?
Albert Einstein solved this problem in 1926 in a paper he wrote on meandering rivers. Einstein was the first person to describe how helical flow helps to determine the length and migration of meander bends in rivers.
Amazon River, 1985
Amazon River, 2014
https:earthobservatory.nasa.gov

## Slide 18: Hydrodynamics

## Slide 19: Important Hydrodynamic Processes
Vertical stratification
Meteorology
  Wind forcing
  Thermal forcing
Water quality
  Affects stratification
Climate
  Long-term effects

## Slide 20: Vertical Stratification
Lakes and reservoirs in temperate climates tend to thermally stratify vertically during the spring and summer. A conceptual model of their stratification divides the water body into three vertical layers:
  The epilimnion, a warm surface layer
  The hypolimnion, a cool bottom layer
  The metalimnion, the layer in between the top and bottom layers. This layer encompasses the thermocline, where the temperature suddenly decreases sharply with depth.
Lake stratification varies continually. It is often described by the depth and strength of the thermocline.
  The seasonal thermocline is characterized by the average depth and strength over a season.
  The diurnal thermocline varies throughout the day.

## Slide 21: Meteorological Forcing
The meteorology of the watershed affects several factors that control the hydrodynamics as well as the water quality of a reservoir.
  Wind forcing: The wind flowing across the reservoir affects depth of stratification, vertical mixing, and circulation (currents across and around the water body).
  Heat balance: The incoming (shortwave) solar radiation and outgoing radiation (longwave radiation, sensible heat, and evaporation) control the heat balance. Wind, solar radiation, and cloud cover, and relative humidity control the evaporation, the largest source of heat loss in a water body.

## Slide 22: Meteorological Forcing: Wind Fetch
The fetch or fetch length of a water body is the length of water over which wind has blown without obstruction.
The fetch varies with the direction of the wind.
If the fetch of the prevailing wind is aligned with the long axis of the water body, then the wind effect on mixing is at its maximum.

## Slide 23: Water Quality Forcing
Water quality affects the clarity of the water:
  Dissolved and particulate matter increase turbidity
Water clarity affects the depth that solar radiation penetrates the water surface.
Clear lakes tend to have deep and relatively cool epilimnions and weak stratification.
Turbid lakes tend to have shallow and warm epilimnions and strong stratification.

## Slide 24: Climate Forcing
Climate change can have a significant affect on reservoir hydrodynamics.
As climate and water temperatures increase, while average wind forcing remains the same, the seasonal stratification will tend to strengthen. This can reduce the tendency of the reservoir to overturn (mix vertically). Poor water quality conditions can intensify in the hypolimnion.
  Example: In Lake Tahoe, a significant quantity of phosphorus is bound with iron in the sediment. Hypoxic conditions could release the phosphorus into the water column, resulting in significant internal loading of phosphorus, increasing algae concentrations.
On the other hand, if climate change increases the strength and frequency of occurrence of intense storms, wind forcing will affect the diurnal stratification. However, extreme precipitation can lead to increased particle inputs from runoff and erosion, which may decrease water clarity.

## Slide 25: Seiches
As wind blows across the water surface, it causes the water surface to tilt. It rises at the downwind side and lowers at the downwind side.
The elevation change is small. For a water body with a fetch of 10 km, the maximum elevation change at the upwind end is only a few centimeters.
When the wind slows down, the water surface tilts in the opposite direction, but it moves past the equilibrium point. This cycle results in a basin-wide standing wave, called a seiche.
Seiches, like other surface waves are relatively fast and shallow.

## Slide 26: Internal Waves
The thermocline can oscillate up and down in response to seicheing, generating internal waves.
The smaller the density difference between two layers of fluid, the larger and slower the waves.
Seiches are small and fast.
Internal waves are large and slow.
Even though they are under the surface, they can be seen from the air and from space.

## Slide 27: Reservoir Processes and Zones
Riverine zone
  River-like flows within channel
  Minimum requirement: 1D river model (segments)
Lacustrine zone
  Lake-like system, vertically stratified, slow flows
  Minimum requirement: 1D reservoir model (layers)
Transition zone
  Stratification and downstream flows important
  Minimum requirement: 2D model (layers and segments)
Reservoir system with important flow, WQ, and ecosystem processes for each of three zones.
Notes:
1D river model used for channels in a reservoir system
2D river model used for floodplain simulation
2D reservoir model used for large stratified reservoirs
Riverine
Transition
Lacustrine
Graphic by Lauren Melendez

## Slide 28: Model Dimensions, River-Reservoir System
Unstratified river/reservoir reaches:
  May be modeled as 1D water bodies (segments)
Stratified reaches:
  May be modeled as 1D reservoirs (layers) for real-time release decision-making to meet downstream objectives
  To characterize and understand in-reservoir processes, reservoirs need to be modeled as 2D water bodies (layers and segments)
    Ensures accuracy, capturing important in-reservoir processes (mixing, pollutants, inflows, etc.)
    Identifies vulnerabilities and restoration/management options (e.g., velocities and temperature for HAB management)
1D River
2D Reservoir
1D Reservoir
1D River
2D Reservoir
1D Reservoir
Graphics by Lauren Melendez

## Slide 29: Model Dimensions: River-Floodplain System
Unstratified river channels are often modeled as 1D water bodies, varying from upstream to downstream
Hydrologic connectivity across the floodplain is important
Floodplains need to be modeled as 2D water bodies, varying in all directions across the landscape
1D River (Channel)
2D River (Floodplain, Wetlands)
Graphics by Lauren Melendez

## Slide 30: Water Quality and Environmental Systems Modeling
Watershed Runoff:
  GSSHA: Surface and sub-surface water quality modeling and Nature-Based Features design tool
  HEC-HMS: Surface runoff temperature modeling
Reservoirs:
  CE-QUAL-W2: 2D reservoir-river hydrodynamics and water quality modeling
  HEC-ResSim: Reservoir operations and water quality modeling
Rivers and Floodplains:
  HEC-RAS: 1D River hydraulics and water quality & vegetation modeling
  ClearWater-Riverine: 2D River-floodplain hydraulics and water quality modeling with HEC-RAS
The Corps Library for Environmental Analysis and Restoration of Watersheds (ClearWater) provides environmental simulation capabilities that leverage existing hydrologic and hydraulic (H&H) models.
Estuary
Temperature
Nutrients
Dissolved Oxygen
Algae
Metals
Contaminants
Riparian Vegetation

## Slide 31: HEC-ResSim Water Quality: Purpose
Need:
  Reservoir operations simulation software capable of integrating environmental objectives into reservoir release decisions
Purpose:
  Fully integrated water quality modeling capabilities in HEC-ResSim enable water quality and related objectives to directly inform reservoir release decision-making, while providing capabilities for watershed-scale ecosystem assessment and management
Flows influence water quality
Water quality influences flows

## Slide 32: HEC-ResSim Water Quality: Approach
Develop fully integrated water quality capabilities into HEC-ResSim (Reservoir System Simulation)
HEC-ResSim simulates reservoir operations at one or more reservoirs for:
  Flood management
  Low flow augmentation
  Water supply
Applications:
  Planning studies
  Detailed reservoir regulation plan investigations
  Real-time decision support

## Slide 33: HEC-ResSim Water Quality Engine
Finite Volume Numerical Scheme
  1D river reach with junctions
  1D vertically stratified reservoir
Explicit solution scheme with sub-stepping
Cell face concentrations determined with 1st order upwind method and 2nd order flux-limiting method
Accept flows computed by hydraulic or hydrologic routing
RMA, “Generalized One-Dimensional Reservoir and River Water Quality Engine Prototype”, prepared for the USACE Hydrologic Engineering Center, November 2017
1D Reach
1D Reservoir

## Slide 34: Water Quality Modeling User Interface
Visualization
Specifying Boundary Conditions
Model Geometry
Constituent Relation Parameters
Operating Rule Priorities
Scripted Rules and State Variables

## Slide 35: Inflow and Water Quality Boundary Conditions
Trinity Lake Inflows
  1-Trinity River, 2-East Fork Trinity, 3-Swift Creek, 4-Stuart Fork
Trinity River Inflows
  5-Rush Cr, 6-Grass Valley Cr, 7-Limekiln, 8-Indian Cr, 9-Weaver Cr, 10-Reading Cr, 11-Douglas City, 12-Browns Cr, 13-Junction City, 14-Canyon Cr, 15-NF Trinity River
Whiskeytown Lake Inflow
  16-Clear Creek above Whiskeytown
Shasta Lake
  17-Sacramento River, 18-McCloud River, 19-Waydalmem Creek, 20-Pit River, 21-Big Backbone Creek
Keswick Reservoir
  22-Spring Creek Debris Dam
Sacramento River to Red Bluff Diversion Dam
  23-Cow Creek, 24-Cottonwood Creek, 25-Battle Creek
Upper Sacramento River System
Prepared by RMA for USBR Water Temperature Modeling Platform (WTMP)

## Slide 36: Meteorologic Boundary Conditions
Upper Sacramento River System
Prepared by RMA for USBR Water Temperature Modeling Platform (WTMP)
Meteorology Station 1: Trinity Center
  Trinity Lake
  Lewiston Lake/Clear Creek Tunnel
  Trinity River to Helena
  Whiskeytown Lake/Spring Creek Tunnel
Meteorology Station 2: Redding Airport
  Shasta Lake
  Keswick Reservoir
  Clear Creek
  Sacramento River to Red Bluff Diversion Dam
Required Meteorology Variables
  Air Temperature
  Wind Speed
  Wind Direction
  Relative Humidity or Dew Point Temperature
  Shortwave Incoming (Downwelling) Radiation
    HEC-ResSim allows this time series to be estimated using the study site’s latitude and longitude and cloudiness data
  Cloudiness

## Slide 37: Temperature and Dissolved Oxygen Simulation with HEC-ResSim Russian River, California Prepared by RMA for the Sonoma County Water Agency
Temperature
Dissolved Oxygen
Lake Sonoma
Lake Mendocino
Temperature
Dissolved Oxygen

## Slide 38: River Temperature and Cold-Water Pool Management with HEC-ResSim Upper Sacramento River, California Prepared by RMA for the U.S. Bureau of Reclamation (USBR)
Shasta Temperature Control Device (TCD) graphic courtesy of Watercourse Engineering
Shasta Lake
Whiskeytown Lake
Trinity Lake
Keswick Dam
Lewiston Dam

## Slide 39: Primary Processes Affecting Temperature in a Vertically Stratified Reservoir
Prepared by RMA for USBR Water Temperature Modeling Platform (WTMP)

## Slide 40: Longitudinal Profile View of a Reservoir-River System
Prepared by RMA for USBR Water Temperature Modeling Platform (WTMP)

## Slide 41: Comparison of HEC-ResSim and CE-QUAL-W2 Model Results Water Temperature Profiles: Shasta Lake, California
Prepared by RMA for USBR Water Temperature Modeling Platform (WTMP)

## Slide 42: Comparison of HEC-ResSim and CE-QUAL-W2 Model Results Water Temperature Profiles: Shasta Lake, California
Statistics | 2014 | 
 | ResSim_T_Mix-2014 | S14-KesW2-River-2014
Mean Bias (°C) | 0.25 | 0.29
MAE (°C) | 0.36 | 0.40
RMSE (°C) | 0.49 | 0.49
Nash-Sutcliffe (NSE) | 0.95 | 0.95
Error Statistics based on comparison with Observed Daily Flow-Weighted Average Tailbay Temperature
Prepared by RMA for USBR Water Temperature Modeling Platform (WTMP)

## Slide 43: HEC-ResSim Water Quality Benefits
HEC-ResSim water quality capabilities support the need for a standardized general-purpose modeling tool to improve environmental assessment, restoration, and management.
Incorporation of water quality (water temperature and constituent concentrations) in HEC-ResSim enables incorporation of water quality and other environmental objectives (such as environmental flows) in the reservoir decision-making process. This allows HEC-ResSim to inform reservoir release decisions, improving model accuracy and delivering high quality multi-objective decision-making to achieve ecosystem benefits.

## Slide 44: HEC-ResSim Water Quality Benefits
Critical downstream habitat will be better managed for water quantity (volume, velocity, depths, etc.) in addition to water quality (water temperature, dissolved oxygen, total dissolved gas, etc.)
Linkage of water quality with multi-objective decision analysis increases project benefits while decreasing modeling and project costs.
HEC-ResSim is often used in real-time decision-making, linked with other models via the Corps Water Management System (CWMS). HEC-ResSim enables water quality objectives to be included in the real-time decision-making process.

## Slide 45: Introduction to CE-QUAL-W2
CE‐QUAL‐W2 is a two‐dimensional (2D), longitudinal/vertical, hydrodynamics and water quality model.
It enables characterization of the vertical and longitudinal changes in a reservoir.
The model assumes the reservoir is ”well mixed” laterally, with no variation from one side of the channel to the other in a given layer (vertical) and segment (longitudinal).
Since CE-QUAL-W2 assumes lateral homogeneity, it is especially suited for relatively long and narrow waterbodies that exhibit longitudinal and vertical water quality gradients.
CE-QUAL-W2 has been applied to rivers, lakes, reservoirs, estuaries, and combinations thereof.
Longitudinal view of temperature output for a riverine section, reservoir, and estuary, from a CE‐QUAL‐W2 model application.

## Slide 46: CE-QUAL-W2 Applications
CE-QUAL-W2 is the reservoir water quality (WQ) model of choice throughout the U.S. and many other countries
CE-QUAL-W2 is the two-dimensional (2D), longitudinal/vertical hydrodynamic and water quality model of choice for the following agencies:
  U.S. Army Corps of Engineers (USACE)
  U.S. Geological Survey (USGS)
  U.S. Bureau of Reclamation (USBR)
  U.S. Environmental Protection Agency (EPA)
  Tennessee Valley Authority (TVA)
There have been more than 300 applications worldwide of CE-QUAL-W2
Cited in more than:
  15 PhD dissertations
  50 Master’s theses
  100 presentations at scientific meetings
  20 journal articles worldwide

## Slide 47: CE-QUAL-W2 Capabilities
Longitudinal-vertical hydrodynamics and water quality in stratified and non-stratified systems
Interactions between nutrients, dissolved oxygen, and organic matter
Fish habitat volume
Selective withdrawal from specially design outlets to provide cold-water releases from stratified reservoirs
Hypolimnetic aeration
Multiple algae, epiphyton/periphyton, zooplankton, and macrophyte groups
CBOD
Sediment diagenesis model
Generic water quality groups
Internal dynamic pipe/culvert model
Hydraulic structures (weirs, spillways) algorithms.

## Slide 48: CE-QUAL-W2 Capabilities, Continued
The hydraulic structures algorithms include submerged and two-way flow over submerged hydraulic structures as well as a dynamic shading algorithm based on topographic and vegetative cover.
Variable density as affected by temperature, salinity, Total Dissolved Solids (TDS), and Total Suspended Solids (TSS) to simulate stratified flow.
28 water quality constituent state variables
  Any combination of constituents can be included or excluded from a simulation.
  The effects of salinity or total dissolved solids/salinity on density, and thus hydrodynamics, are included only when simulated in the water quality module.
  The water quality algorithm is modular, allowing constituents to be easily added as additional subroutines.

## Slide 49: CE-QUAL-W2 Benefits
CE‐QUAL‐W2 simulates two‐dimensional (2D), longitudinal/vertical, hydrodynamics and water quality.
  Enables characterization of the vertical and longitudinal changes in a reservoir.
  Capable of resolving longitudinal gradients due to discharges, low residence time, etc.
  Especially suited to long and narrow reservoirs that exhibit longitudinal and vertical water quality gradients. Longitudinal gradients may be caused by point source discharges or low residence time.
Widely used by USACE, USGS, USBR, and state and local agencies for environmental impact assessments, planning studies, etc.
Used as a research tool by researchers at universities and other organizations. At least 1,500 publications have utilized or referenced CE-QUAL-W2 in the year 2022 alone.
  “The number of publications that focused on water quality simulations using CE-QUAL-W2 ranked first most often, reaching 22 in 2020.” – Bai et al. (2022). Assessment and a review of research on surface water quality modeling. Ecological Modelling.
Open source and public domain. ERDC maintains the official version of the program. Users may freely edit the source code for custom applications.
Supported by the HH&C SET numerical model maintenance program
Longitudinal view of temperature output for a riverine section, reservoir, and estuary, from a CE‐QUAL‐W2 model application.

## Slide 50
HEC-RAS River Water Quality (1D)
The USACE Hydrologic Engineering Center’s River Analysis System (HEC-RAS) simulates one- and two-dimensional (1D and 2D) river hydraulics:
  Computes river velocities, stages, profiles, and inundated areas (with RAS Mapper) given stream flow and geometry
  Industry standard hydraulic tool used worldwide
  100,000 worldwide downloads per year
  One-dimensional (1D) water quality capabilities allow environmental impacts assessments in rivers and streams

## Slide 51: HEC-RAS-2D: Hydrodynamic Simulations
HEC-RAS can perform two-dimensional (2D) hydrodynamic routing within the unsteady flow analysis portion of the program.
2D flow areas in HEC-RAS can be used in several ways. The following are examples of how 2D flow areas can be used to support modeling with HEC-RAS:
  Detailed 2D channel modeling
  Detailed 2D channel and floodplain modeling
  Multiple 2D flow areas in the same geometry
  Directly connect multiple 2D flow areas with hydraulic structures
  Mixed flow regime. The 2D capability (as well as the 1D) can handle supercritical and subcritical flow, as well as the flow transitions from subcritical to super critical and super critical to subcritical (hydraulic jumps).
2D flow modeling is accomplished by adding 2D flow area elements into the HEC-RAS model in the same manner as adding a storage area.
A 2D flow area is added by following these steps:
  Drawing a 2D flow area polygon
  Developing the 2D computational mesh
  Linking the 2D flow areas to 1D model elements and/or directly connecting boundary conditions to the 2D areas.

## Slide 52: ClearWater-Riverine
The ERDC Environmental Laboratory (ERDC-EL) is developing a state-of-the-art water quality modeling system, Clearwater-Riverine, that simulates temperature and advanced nutrient cycling in branching river systems and floodplains, incorporating hydrodynamic, water quality, and meteorologic inputs from multiple data sources and models.
ClearWater-Riverine will enable the evaluation of system vulnerabilities and identification of adaptation pathways to improve the resilience of floodplain ecosystems to environmental stresses, which include increasing frequency and intensity of extreme precipitation events and decreasing freshwater flows.
Water quality kinetics, heat budget, and transport simulation capabilities in ClearWater-Riverine are furnished by ERDC's ClearWater modules.
The ClearWater-Riverine framework links the capabilities provided by the ClearWater modules and advection-diffusion engine with the two-dimensional (2D) HEC-RAS model.
HEC-RAS models have been developed for most of the watersheds around the world. By leveraging these existing models, ClearWater-Riverine provides a cost-effective, data-driven tool for impact assessment, planning studies, and the restoration and management of aquatic ecosystems.

## Slide 53: ClearWater-Riverine: 2D Water Quality Modeling with HEC-RAS
Inputs
  HEC-RAS-2D Model Data
  Volumetric flows, velocities, depths
  Model grid (bathymetry)
  Observed meteorology and water quality time series
ClearWater water quality modules
  Compute heat budget and constituent kinetics for each cell
Water Quality Engine
  Computes advection-diffusion across the model grid at each time step
Outputs
  Time series of 2D water quality grids, one time series per variable
  Time series of simulated hydrodynamic and water quality data at user-selected locations
Framework
  Controls model input and output
  Controls the computational, input, and output time steps
  Controls simulation across the model grid
  Coordinates engine, modules, and data

## Slide 54: ClearWater-Riverine: Water Quality Modeling of Complex Channels and Floodplains with HEC-RAS-2D

## Slide 55: ClearWater-Riverine: Water Quality Modeling of Complex Channels and Floodplains with HEC-RAS-2D

## Slide 56: Gridded Surface Subsurface Hydrologic Analysis Program (GSSHA)

## Slide 57: What is GSSHA?
GSSHA is a complete watershed simulation and management model used for hydrologic, hydraulic, sediment and quality simulation and management.
GSSHA is a fully distributed, physics-based (process-based, deterministic) model that utilizes a grid to represent the watershed.
GSSHA is a product of the ERDC Coastal and Hydraulics Laboratory (CHL)
  Maintained
  Supported
  Distributed
GSSHA is a direct descendent of the surface water hydrologic model CASC2D developed at Colorado State University.

## Slide 58: GSSHA Benefits for Modeling NNBF Design
Ability to simulate physical processes and spatial variability across the landscape:
  Provides more accurate model results
  Enables better representation of future alternatives, where the system may change in ways that have not been captured by past observations and measurements.

## Slide 59: Physically Based Parameters
Values are based on physical conditions:
  Extendible beyond calibration range
  May reduce amount of calibration data needed relative to empirical and stochastic methods
The ability to simulate the complex dynamics of actual physical conditions provides a means to logically alter parameters based on changing conditions.
  Land use changes
  Project alternatives
  Climate change

## Slide 60
Sediment
Sediment-Water
Transfer
Outflow
Dispersion
Inflow
Dispersion
Atmospheric
Transfer
Heat Withdrawal
Heat Load
i
Channel Reach
Q = Flows
V = Volumes
E = Dispersions
Water Temperature: Channels

## Slide 61
ET
Flow In/Out of Cell
Flow In/Out of Cell
Surface/Sub-Surface Interactions
Precipitation
i
Overland Cell
Q = Flows
V = Volumes
E = Dispersions
Water Temperature: Overland Flow (Runoff)

## Slide 62
Radiation Terms
Non-Radiation Terms
Net Absorbed Radiation
Water Dependent Terms
Solar
Shortwave
Radiation
Atmospheric
Longwave
Radiation
Water
Longwave
Radiation
Conduction
and
Convection
Evaporation
and
Condensation
Water Temperature: Air-Water Heat Flux

## Slide 63: Water Quality Modeling Team Members and Contributors (Alphabetical)
Lea Adams, HEC
Steve Andrews, RMA
Anthony Aufdenkampe, LimnoTech
Sitlaly Avelino, USACE - Sacramento
Chris Berger, Portland State University
Tom Brauer, HEC
Barry Bunch, ERDC-EL
Aaron Byrd, ERDC-CHL
Haley Canham, USACE - Sacramento
John DeGeorge, RMA
Tim Dekker, LimnoTech
Mitch Delcau, Colorado State University
Chuck Downer, ERDC-CHL
Samantha Eanes, USACE - Sacramento
Paul Ely, RMA
Trudy Estes, ERDC-EL
Christine Hoffmann, USACE - Sacramento
Joan Klipsch, HEC
John Kucharski, ERDC-EL
Zach Jelenek, USACE – Sacramento
Mark Jensen, HEC
Billy Johnson, LimnoTech
Nancy Lam, USACE - Sacramento District
Shannon Larson, RMA
Cindy Lowney, RMA
Lauren Melendez, ERDC-EL
Ryan Miles, RMA
Alexis Mills, USACE – Northwest Division
Isaac Mudge, USACE – New Orleans / ERDC
Jennifer Olszewski, ERDC-EL
Leila Ostadrahimi, HEC
Greg Peterson, LimnoTech
Steve Piper, RMA
Nawa Pradhan, ERDC-CHL
Patrick Ray, University of Cincinnati
Daniel Rucinski, LimnoTech
Jason Rutyna, LimnoTech
Jodi Ryder, ERDC-EL
Terra Salamida, USACE - Sacramento
Alex Sanchez, HEC
Rahat Saiful, University of Cincinnati
Jonathan Sorunke, USACE - Sacramento
Tad Slawecki, LimnoTech
Don Smith, RMA
Julia Slaughter, HEC
John Sourbeer, USACE – Pittsburgh
Todd Steissberg, ERDC-EL
Kathryn Tackley, USACE – Portland
Jordan Thennis, USACE - Sacramento
Tammy Threadgill, LimnoTech
Dottie Tillman, USACE-ERDC-EL
Dan Turner, USACE – Northwest Division
Scott Wells, Portland State University
Brian Zettle, USACE – USACE - TNTCX
Kelsey Walak, USACE - Sacramento
Zhonglong Zhang, Portland State University

## Slide 64: Questions?